## Slide 1: Digital Transmission

## Slide 2: 4-2 ANALOG-TO-DIGITAL CONVERSION
A digital signal is superior to an analog signal because it is more robust to noise and can easily be recovered, corrected and amplified. For this reason, the tendency today is to change an analog signal to digital data. In this section we describe two techniques, pulse code modulation and delta modulation.
Topics discussed in this section:
Pulse Code Modulation (PCM)

## Slide 3: PCM
PCM consists of three steps to digitize an analog signal:
  Sampling
  Quantization
  Binary encoding
Before we sample, we have to filter the signal to limit the maximum frequency of the signal as it affects the sampling rate.
Filtering should ensure that we do not distort the signal, ie remove high frequency components that affect the signal shape.

## Slide 4: Figure 4.21 Components of PCM encoder

## Slide 5: Sampling
Sampling is defined as, “The process of measuring the instantaneous values of continuous-time signal in a discrete form.”
Analog signal is sampled every TS secs.
Ts (sampling time) is referred to as the sampling interval.
fs = 1/Ts is called the sampling rate or sampling frequency.
There are 3 sampling methods:
  Ideal - an impulse at each sampling instant
  Natural - a pulse of short width with varying
amplitude
  Flattop - sample and hold, like natural but with single amplitude value
The process is referred to as (Pulse Amplitude Modulation) PAM and the outcome is a signal with analog (non integer) values

## Slide 6: Figure 4.22 Three different sampling methods for PCM

## Slide 7: Note
According to the Nyquist theorem, the sampling rate must be
at least 2 times the highest frequency contained in the signal.

## Slide 8: Figure 4.23 Nyquist sampling rate for low-pass and bandpass signals

## Slide 9: Quantization
Quantization is representing the sampled values of the amplitude by a finite set of levels, which means converting a continuous-amplitude sample into a discrete-time signal.
Sampling results in a series of pulses of varying amplitude values ranging between two limits: a min and a max.
The amplitude values are infinite between the two limits.
We need to map the infinite amplitude values onto a finite set of known values.
This is achieved by dividing the distance between min and max into L zones, each of height 
 = (max - min)/L

## Slide 10: Quantization Levels
The midpoint of each zone is assigned a value from 0 to L-1 (resulting in L values)
Each sample falling in a zone is then approximated to the value of the midpoint.

## Slide 11: Quantization Zones
Assume we have a voltage signal with amplitutes Vmin=-20V and Vmax=+20V.
We want to use L=8 quantization levels.
Zone width  = (20 - -20)/8 = 5
The 8 zones are: -20 to -15, -15 to -10,
-10 to -5, -5 to 0, 0 to +5, +5 to +10,
+10 to +15, +15 to +20
The midpoints are: -17.5, -12.5, -7.5, -
2.5, 2.5, 7.5, 12.5, 17.5

## Slide 12: Figure 4.26 Quantization and encoding of a sampled signal

## Slide 13: Quantization Error
When a signal is quantized, we introduce an error - the coded signal is an approximation of the actual amplitude value.
The difference between actual and coded value (midpoint) is referred to as the quantization error.
The more zones, the smaller  which results in smaller errors.
BUT, the more zones the more bits required to encode the samples -> higher bit rate

## Slide 14: Bit rate and bandwidth requirements of PCM
The bit rate of a PCM signal can be calculated form
the number of bits per sample x the sampling rate
Bit rate = nb x fs
The bandwidth required to transmit this signal depends on the type of line encoding used. Refer to previous section for discussion and formulas.
A digitized signal will always need more bandwidth than the original analog signal. Price we pay for robustness and other features of digital transmission.