## Slide 1
What is classless addressing?
Classless addressing is an IPv4 addressing architecture that uses variable-length subnet masking.
Classless Addressing
To reduce the wastage of IP addresses in a block, we use sub-netting. What we do is that we use host id bits as net id bits of a classful IP address. We give the IP address and define the number of bits for mask along with it (usually followed by a ‘/’ symbol), like, 192.168.1.1/28. Here, subnet mask is found by putting the given number of bits out of 32 as 1, like, in the given address, we need to put 28 out of 32 bits as 1 and the rest as 0, and so, the subnet mask would be 255.255.255.240.

## Slide 2: Note
The first address in the block can be found by setting the rightmost 32 − n bits to 0s.
19.2

## Slide 3: A block of addresses is granted to a small organization. We know that one of the addresses is 205.16.37.39/28. What is the first address in the block?
19.3
Solution
The binary representation of the given address is 11001101 00010000 00100101 00100111
If we set 32−28 rightmost bits to 0, we get
11001101 00010000 00100101 0010000
or 205.16.37.32.
This is actually the block shown in Figure 19.3.
Example 19.6

## Slide 4: Note
The last address in the block can be found by setting the rightmost 32 − n bits to 1s.
19.4

## Slide 5: Find the last address for the block in Example 19.6.
19.5
Solution
The binary representation of the given address is 11001101 00010000 00100101 00100111
If we set 32 − 28 rightmost bits to 1, we get 11001101 00010000 00100101 00101111
or 205.16.37.47
This is actually the block shown in Figure 19.3.
Example 19.7

## Slide 6: Note
The number of addresses in the block can be found by using the formula 232−n.
19.6

## Slide 7: Find the number of addresses in Example 19.6.
19.7
Example 19.8
Solution
The value of n is 28, of addresses is 2 32−28 or 16.
which
means
that
number

## Slide 8: Another way to find the first address, the last address, and
19.8
the number of addresses is to represent the mask as a 32-bit binary (or 8-digit hexadecimal) number. This is particularly useful when we are writing a program to find these pieces of information. In Example 19.5 the /28 can be represented as
11111111 11111111 11111111 11110000
(twenty-eight 1s and four 0s).
Find
The first address
The last address
The number of addresses.
Example 19.9

## Slide 9: Solution
a. The first address can be found by ANDing the given addresses with the mask. ANDing here is done bit by bit. The result of ANDing 2 bits is 1 if both bits are 1s; the result is 0 otherwise.
Example 19.9 (continued)

## Slide 10: Example 19.9 (continued)
b. The last address can be found by ORing the given addresses with the complement of the mask. ORing here is done bit by bit. The result of ORing 2 bits is 0 if both bits are 0s; the result is 1 otherwise. The complement of a number is found by changing each 1 to 0 and each 0 to 1.

## Slide 11: c. The number
of addresses can be found by
decimal
complementing the mask, interpreting it as a number, and adding 1 to it.
Example 19.9 (continued)

## Slide 12: Figure 19.4 A network configuration for the block 205.16.37.32/28

## Slide 13: Note
The first address in a block is normally not assigned to any device;
it is used as the network address that represents the organization
to the rest of the world.

## Slide 14: Figure 19.5 Two levels of hierarchy in an IPv4 address

## Slide 15: Figure 19.6 A frame in a character-oriented protocol

## Slide 16: Note
Each address in the block can be considered as a two-level hierarchical structure:
the leftmost n bits (prefix) define the network;
the rightmost 32 − n bits define
the host.

## Slide 17: Figure 19.7 Configuration and addresses in a subnetted network

## Slide 18: Figure 19.8 Three-level hierarchy in an IPv4 address

## Slide 19
An ISP is granted a block of addresses starting with 190.100.0.0/16 (65,536 addresses). The ISP needs to distribute these addresses to three groups of customers as follows:
The first group has 64 customers; each needs 256 addresses.
The second group has 128 customers; each needs 128 addresses.
The third group has 128 customers; each needs 64 addresses.
Design the subblocks and find out how many addresses are still available after these allocations.
Example 19.10

## Slide 20: Solution Figure 19.9 shows the situation.
Example 19.10 (continued)
Group 1
For this group, each customer needs 256 addresses. This means that 8 (log2 256) bits are needed to define each host. The prefix length is then 32 − 8 = 24. The addresses are

## Slide 21: Group 2 For this group, each customer needs 128 addresses. This means that 7 (log2 128) bits are needed to define each host. The prefix length is then 32 − 7 = 25. The addresses are
Example 19.10 (continued)

## Slide 22: Group 3
Example 19.10 (continued)
For this group, each customer needs 64 addresses. This means that 6 (log264) bits are needed to each host. The prefix length is then 32 − 6 = 26. The addresses are
Number of granted addresses to the ISP: 65,536 Number of allocated addresses by the ISP: 40,960 Number of available addresses: 24,576

## Slide 23: Figure 19.9 An example of address allocation and distribution by an ISP