## Slide 1: DATA AND SIGNALS
3.1

## Slide 2: To be transmitted, data must be transformed to electromagnetic signals.

## Slide 3: ANALOG AND DIGITAL
Data can be analog or digital. The term analog data refers to information that is continuous; digital data refers to information that has discrete states. Analog data take on continuous values. Digital data take on discrete values.
Topics discussed in this section:
Analog and Digital Data Analog and Digital Signals
Periodic and Nonperiodic Signals

## Slide 4: Data can be analog or digital. Analog data are continuous and take continuous values.
Note
Digital data have discrete states and take discrete values.

## Slide 5: Signals can be analog or digital. Analog signals can have an infinite number of values in a range; digital signals can have only a limited number of values.
Note

## Slide 6: Comparison of analog and digital signals

## Slide 7: Note
In data communications, we commonly use periodic analog signals and nonperiodic digital signals.
3.7

## Slide 8: 3-2 PErIoDIc ANAloG SIGNAlS
Periodic analog signals can be classified as simple or composite.
Sine Wave Wavelength
Time and Frequency Domain Composite Signals Bandwidth
3.8

## Slide 9: Figure 3.2 A sine wave
3.9

## Slide 10: Note
We discuss a mathematical approach to sine waves in Appendix C.

## Slide 11: Example 3.1
The power in your house can be represented by a sine wave with a peak amplitude of 155 to 170 V. However, it is common knowledge that the voltage of the power in
U.S. homes is 110 to 120 V. This discrepancy is due to the fact that these are root mean square (rms) values. The signal is squared and then the average amplitude is calculated. The peak value is equal to 2½ × rms value.

## Slide 12: Figure 3.3 Two signals with the same phase and frequency, but different amplitudes

## Slide 13: Example 3.2
The voltage of a battery is a constant; this constant value can be considered a sine wave, as we will see later. For example, the peak value of an AA battery is normally
1.5 V.

## Slide 14: Note
Frequency and period are the inverse of each other.

## Slide 15: Figure 3.4 Two signals with the same amplitude and phase, but different frequencies

## Slide 16: Table 3.1 Units of period and frequency

## Slide 17
The power we use at home has a frequency of 60 Hz. The period of this sine wave can be determined as follows:
Example 3.3

## Slide 18: Example 3.4
Express a period of 100 ms in microseconds.
Solution

## Slide 19: Example 3.5
The period of a signal is 100 ms. What is its frequency in kilohertz?
Solution

## Slide 20: Note
Frequency is the rate of change with respect to time.
Change in a short span of time means high frequency.
Change over a long span of time means low frequency.

## Slide 21: Note
If a signal does not change at all, its frequency is zero.
If a signal changes instantaneously, its frequency is infinite.

## Slide 22: Note
Phase describes the position of the waveform relative to time 0.

## Slide 23: Figure 3.5 Three sine waves with the same amplitude and frequency, but different phases

## Slide 24: Example 3.6
A sine wave with value 1/6 cycle with respect to time 0. What is its phase in degrees and radians?
Solution

## Slide 25: Figure 3.6 Wavelength and period

## Slide 26: Wavelength
Wavelength is the distance a signal can travel in one period.
Wavelength= propagation speed* period
Or
Wavelength= propagation speed/ frequency

## Slide 27: Figure 3.7 The time-domain and frequency-domain plots of a sine wave

## Slide 28: Note
A complete sine wave in the time domain can be represented by one single spike in the frequency domain.

## Slide 29: Example 3.7
The frequency domain is more compact and useful when we are dealing with more than one sine wave. For example, Figure 3.8 shows three sine waves, each with different amplitude and frequency. All can be represented by three spikes in the frequency domain.

## Slide 30: Figure 3.8 The time domain and frequency domain of three sine waves

## Slide 31
A single-frequency sine wave is not useful in data communications;
we need to send a composite signal, a signal made of many simple sine waves.
Note

## Slide 32: According to Fourier analysis, any composite signal is a combination of simple sine waves with different frequencies, amplitudes, and phases. Fourier analysis is discussed in Appendix C.
Note

## Slide 33: If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies; if the composite signal is nonperiodic, the decomposition gives a combination of sine waves with continuous frequencies.
Note

## Slide 34: Example 3.8
Figure 3.9 shows a periodic composite signal with frequency f. This type of signal is not typical of those found in data communications. We can consider it to be three alarm systems, each with a different frequency. The analysis of this signal can give us a good understanding of how to decompose signals.

## Slide 35: Figure 3.9 A composite periodic signal

## Slide 36: Figure 3.10 Decomposition of a composite periodic signal in the time and frequency domains

## Slide 37: Example 3.9
Figure 3.11 shows a nonperiodic composite signal. It can be the signal created by a microphone or a telephone set when a word or two is pronounced. In this case, the composite signal cannot be periodic, because that implies that we are repeating the same word or words with exactly the same tone.

## Slide 38: Figure 3.11 The time and frequency domains of a nonperiodic signal

## Slide 39
The bandwidth of a composite signal is the difference between the
highest and the lowest frequencies contained in that signal.
Note

## Slide 40: Figure 3.12 The bandwidth of periodic and nonperiodic composite signals

## Slide 41: Example 3.10
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is its bandwidth? Draw the spectrum, assuming all components have a maximum amplitude of 10 V. Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
The spectrum has only five spikes, at 100, 300, 500, 700,
and 900 Hz (see Figure 3.13).

## Slide 42: Figure 3.13 The bandwidth for Example 3.10

## Slide 43: Example 3.11
A periodic signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all frequencies of the same amplitude.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
The spectrum contains all integer frequencies. We show this by a series of spikes (see Figure 3.14).

## Slide 44: Figure 3.14 The bandwidth for Example 3.11

## Slide 45: Example 3.12
A nonperiodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V. The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal.
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz. Figure 3.15 shows the frequency domain and the bandwidth.

## Slide 46: Figure 3.15 The bandwidth for Example 3.12

## Slide 47: Example 3.13
An example of a nonperiodic composite signal is the signal propagated by an AM radio station. In the United States, each AM radio station is assigned a 10-kHz bandwidth. The total bandwidth dedicated to AM radio ranges from 530 to 1700 kHz. We will show the rationale behind this 10-kHz bandwidth in Chapter 5.

## Slide 48: Example 3.14
Another example of a nonperiodic composite signal is the signal propagated by an FM radio station. In the United States, each FM radio station is assigned a 200- kHz bandwidth. The total bandwidth dedicated to FM radio ranges from 88 to 108 MHz. We will show the rationale behind this 200-kHz bandwidth in Chapter 5.

## Slide 49: Example 3.15
Another example of a nonperiodic composite signal is the signal received by an old-fashioned analog black- and-white TV. A TV screen is made up of pixels. If we assume a resolution of 525 × 700, we have 367,500 pixels per screen. If we scan the screen 30 times per second, this is 367,500 × 30 = 11,025,000 pixels per second. The worst-case scenario is alternating black and white pixels. We can send 2 pixels per cycle. Therefore, we need 11,025,000 / 2 = 5,512,500 cycles per second, or Hz. The bandwidth needed is 5.5125 MHz.

## Slide 50: 3-3 DIGItAl SIGNAlS
In addition to being represented by an analog signal, information can also be represented by a digital signal. For example, a 1 can be encoded as a positive voltage and a 0 as zero voltage. A digital signal can have more than two levels. In this case, we can send more than 1 bit for each level.
Topics discussed in this section:
Bit Rate Bit Length
Digital Signal as a Composite Analog Signal Application Layer

## Slide 51: Figure 3.16 Two digital signals: one with two signal levels and the other with four signal levels

## Slide 52: Note
Appendix C reviews information about exponential and
logarithmic functions.
Appendix C reviews information about exponential and logarithmic functions.

## Slide 53: Example 3.16
A digital signal has eight levels. How many bits are needed per level? We calculate the number of bits from the formula
Each signal level is represented by 3 bits.

## Slide 54: Example 3.17
A digital signal has nine levels. How many bits are needed per level? We calculate the number of bits by using the formula. Each signal level is represented by
3.17 bits. However, this answer is not realistic. The number of bits sent per level needs to be an integer as well as a power of 2. For this example, 4 bits can represent one level.

## Slide 55: Bit Rate
Most Digital Signals are non-periodic. Therefore, period and frequency are not appropriate characteristics.
Bit rate is used.
Bit rate is number of bits sent in 1s. Expressed in
bps.

## Slide 56: Example 3.18
Assume we need to download text documents at the rate of 100 pages per minute. What is the required bit rate of the channel?
Solution
A page is an average of 24 lines with 80 characters in each line. If we assume that one character requires 8 bits, the bit rate is

## Slide 57: Example 3.19
A digitized voice channel, as we will see in Chapter 4, is made by digitizing a 4-kHz bandwidth analog voice signal. We need to sample the signal at twice the highest frequency (two samples per hertz). We assume that each sample requires 8 bits. What is the required bit rate?
Solution
The bit rate can be calculated as

## Slide 58: Example 3.20
What is the bit rate for high-definition TV (HDTV)?
Solution
HDTV uses digital signals to broadcast high quality video signals. The HDTV screen is normally a ratio of 16 : 9. There are 1920 by 1080 pixels per screen, and the screen is renewed 30 times per second. Twenty-four bits represents one color pixel.
The TV stations reduce this rate to 20 to 40 Mbps through compression.

## Slide 59: Bit Length
Bit length is distance one bit occupies on transmission medium.
Bit length= propagation speed* bit duration

## Slide 60: Figure 3.18 Baseband transmission

## Slide 61: Note
A digital signal is a composite analog signal with an infinite bandwidth.

## Slide 62: Figure 3.19 Bandwidths of two low-pass channels

## Slide 63: Figure 3.20 Baseband transmission using a dedicated medium

## Slide 64: Note
Baseband transmission of a digital signal that preserves the shape of the digital signal is possible only if we have a low-pass channel with an infinite or very wide bandwidth.

## Slide 65: Note
In baseband transmission, the required bandwidth is
proportional to the bit rate;
if we need to send bits faster, we need more bandwidth.
3.66
In baseband transmission, the required bandwidth is proportional to the bit rate; if we need to send bits faster, we need more bandwidth.

## Slide 66: Broadband Transmission: Bandwidth of a bandpass channel

## Slide 67: Note
If the available channel is a bandpass channel, we cannot send the digital signal directly to the channel;
we need to convert the digital signal to an analog signal before transmission.

## Slide 68: Figure 3.24 Modulation of a digital signal for transmission on a bandpass channel

## Slide 69: Example 3.24
An example of broadband transmission using modulation is the sending of computer data through a telephone subscriber line, the line connecting a resident to the central telephone office. These lines are designed to carry voice with a limited bandwidth. The channel is considered a bandpass channel. We convert the digital signal from the computer to an analog signal, and send the analog signal. We can install two converters to change the digital signal to analog and vice versa at the receiving end. The converter, in this case, is called a modem which we discuss in detail in Chapter 5.

## Slide 70: Example 3.25
A second example is the digital cellular telephone. For better reception, digital cellular phones convert the analog voice signal to a digital signal (see Chapter 16). Although the bandwidth allocated to a company providing digital cellular phone service is very wide, we still cannot send the digital signal without conversion. The reason is that we only have a bandpass channel available between caller and callee. We need to convert the digitized voice to a composite analog signal before sending.

## Slide 71: DAtA rAtE lIMItS
A very important consideration in data communications is how fast we can send data, in bits per second, over a channel. Data rate depends on three factors:
The bandwidth available
The level of the signals we use
The quality of the channel (the level of noise)
Topics discussed in this section: Noiseless Channel: Nyquist Bit Rate Noisy Channel: Shannon Capacity Using Both Limits

## Slide 72: Note
Increasing the levels of a signal may reduce the reliability of the system.

## Slide 73: Example 3.33
Does the Nyquist theorem bit rate agree with the intuitive bit rate described in baseband transmission?
Solution
They match when we have only two levels. We said, in baseband transmission, the bit rate is 2 times the bandwidth if we use only the first harmonic in the worst case. However, the Nyquist formula is more general than what we derived intuitively; it can be applied to baseband transmission and modulation. Also, it can be applied when we have two or more levels of signals.

## Slide 74
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. The maximum bit rate can be calculated as
Example 3.34

## Slide 75
Consider the same noiseless channel transmitting a signal with four signal levels (for each level, we send 2 bits). The maximum bit rate can be calculated as
Example 3.35

## Slide 76: Example 3.36
We need to send 265 kbps over a noiseless channel with a bandwidth of 20 kHz. How many signal levels do we need?
Solution
We can use the Nyquist formula as shown:
Since this result is not a power of 2, we need to either increase the number of levels or reduce the bit rate. If we have 128 levels, the bit rate is 280 kbps. If we have 64 levels, the bit rate is 240 kbps.

## Slide 77: Example 3.37
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero. In other words, the noise is so strong that the signal is faint. For this channel the capacity C is calculated as
This means that the capacity of this channel is zero regardless of the bandwidth. In other words, we cannot receive any data through this channel.

## Slide 78: Example 3.38
We can calculate the theoretical highest bit rate of a regular telephone line. A telephone line normally has a bandwidth of 3000. The signal-to-noise ratio is usually 3162. For this channel the capacity is calculated as
This means that the highest bit rate for a telephone line is 34.860 kbps. If we want to send data faster than this, we can either increase the bandwidth of the line or improve the signal-to-noise ratio.

## Slide 79: Example 3.39
The signal-to-noise ratio is often given in decibels. Assume that SNRdB = 36 and the channel bandwidth is 2 MHz. The theoretical channel capacity can be calculated as

## Slide 80: Example 3.40
For practical purposes, when the SNR is very high, we can assume that SNR + 1 is almost the same as SNR. In these cases, the theoretical channel capacity can be simplified to
For example, we can calculate the theoretical capacity of the previous example as

## Slide 81: Example 3.41
We have a channel with a 1-MHz bandwidth. The SNR for this channel is 63. What are the appropriate bit rate and signal level?
Solution
First, we use the Shannon formula to find the upper limit.

## Slide 82: Example 3.41 (continued)
The Shannon formula gives us 6 Mbps, the upper limit. For better performance we choose something lower, 4 Mbps, for example. Then we use the Nyquist formula to find the number of signal levels.

## Slide 83: Note
The Shannon capacity gives us the upper limit; the Nyquist formula tells us how many signal levels we need.

## Slide 84: 3-6 PErForMANcE
One important issue in networking is the performance of the network—how good is it? We discuss quality of service, an overall measurement of network performance, in greater detail in Chapter 24. In this section, we introduce terms that we need for future chapters.
Topics discussed in this section:
Bandwidth Throughput Latency (Delay)
Bandwidth-Delay Product

## Slide 85: Note
In networking, we use the term bandwidth in two contexts.
❏ The | first, bandwidth in hertz, | refers | to
the | range of frequencies | in | a
range of
composite frequencies
signal that a
or the channel can
pass.
❏ The
second, refers to the speed of
second, bandwidth in bits per
bit
transmission in a channel or link.

## Slide 86: Example 3.42
The bandwidth of a subscriber line is 4 kHz for voice or data. The bandwidth of this line for data transmission can be up to 56,000 bps using a sophisticated modem to change the digital signal to analog.

## Slide 87: Example 3.43
If the telephone company improves the quality of the line and increases the bandwidth to 8 kHz, we can send 112,000 bps by using the same technology as mentioned in Example 3.42.

## Slide 88: Example 3.44
A network with bandwidth of 10 Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000 bits. What is the throughput of this network?
Solution
We can calculate the throughput as
The throughput is almost one-fifth of the bandwidth in this case.

## Slide 89: Example 3.45
What is the propagation time if the distance between the two points is 12,000 km? Assume the propagation speed to be 2.4 × 108 m/s in cable.
Solution
We can calculate the propagation time as
The example shows that a bit can go over the Atlantic Ocean in only 50 ms if there is a direct cable between the source and the destination.

## Slide 90: Example 3.46
What are the propagation time and the transmission time for a 2.5-kbyte message (an e-mail) if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
We can calculate the propagation and transmission time as shown on the next slide:

## Slide 91: Example 3.46 (continued)
Note that in this case, because the message is short and the bandwidth is high, the dominant factor is the propagation time, not the transmission time. The transmission time can be ignored.

## Slide 92: Example 3.47
What are the propagation time and the transmission time for a 5-Mbyte message (an image) if the bandwidth of the network is 1 Mbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
We can calculate the propagation and transmission times as shown on the next slide.

## Slide 93: Example 3.47 (continued)
Note that in this case, because the message is very long and the bandwidth is not very high, the dominant factor is the transmission time, not the propagation time. The propagation time can be ignored.