## Slide 1: Digital Transmission

## Slide 2: 4-1 DIGITAL-TO-DIGITAL CONVERSION
In this section, we see how we can represent digital data by using digital signals. The conversion involves
three techniques: line coding, block coding, scrambling. Line coding is always needed;
and block
coding and scrambling may or may not be needed.
Topics discussed in this section:
Line Coding
Line Coding Schemes
Block Coding
Scrambling

## Slide 3: Line Coding
Converting a string of 1‟s and 0‟s (digital data) into a sequence of signals that denote the 1‟s and 0‟s.
For example a high voltage level (+V) could represent a “1” and a low voltage level (0 or -V) could represent a “0”.

## Slide 4: Figure 4.1 Line coding and decoding

## Slide 5: Mapping Data symbols onto Signal levels
A data symbol (or element) can consist of a number of data bits:
  1 , 0 or
  11, 10, 01, ……
A data symbol can be coded into a single signal element or multiple signal elements

## Slide 6: Relationship between data rate and signal rate
The data rate defines the number of bits sent per sec - bps. It is often referred to the bit rate.
The signal rate is the number of signal elements sent in a second and is measured in bauds. It is also referred to as the modulation rate.
Goal is to increase the data rate whilst reducing the baud rate.

## Slide 7: Figure 4.2 Signal element versus data element

## Slide 8: Data rate and Baud rate
The baud or signal rate can be expressed as:
S = c x N x 1/r bauds where N is data rate
c is the case factor (worst, best & avg.)
r is the ratio between data element &
signal element

## Slide 9: Example 4.1
A signal is carrying data in which one data element is encoded as one signal element ( r = 1). If the bit rate is 100 kbps, what is the average value of the baud rate if c is between 0 and 1?
Solution
We assume that the average value of c is 1/2 . The baud rate is then

## Slide 10: Considerations for choosing a good signal element referred to as line encoding

## Slide 11: Line encoding C/Cs
DC(Data Current) Component:- the average amplitude of a unipolar encoded signal in nonzero. This creates what is called DC(direct signal component) a component with nonzero frequency.

## Slide 12: Line encoding C/Cs
Self synchronization – When a signal is unvarying, the receiver cannot determine the beginning and ending of each bit.

## Slide 13: Figure 4.3 Effect of lack of synchronization

## Slide 14: Example 4.3
In a digital transmission, the receiver clock is 0.1 percent faster than the sender clock. How many extra bits per second does the receiver receive if the data rate is 1 kbps? How many if the data rate is 1 Mbps?
Solution
At 1 kbps, the receiver receives 1001 bps instead of 1000 bps.
At 1 Mbps, the receiver receives 1,001,000 bps instead of 1,000,000 bps.

## Slide 15: Line encoding
Error detection - errors occur during transmission due to line impairments.
Some codes are constructed such that when an error occurs it can be detected. For example: a particular signal transition is not part of the code. When it occurs, the receiver will know that a symbol error has occurred.

## Slide 16: Line encoding
Noise and interference - there are line encoding techniques that make the transmitted signal “immune” to noise and interference.
This means that the signal cannot be corrupted, it is stronger than error detection.

## Slide 17: Line encoding
Complexity - the more robust and resilient the code, the more complex it is to implement and the price is often more than simple one.

## Slide 18: Figure 4.4 Line coding schemes

## Slide 19: Unipolar
All signal levels are on one side of the time axis - either above or below
NRZ - Non Return to Zero scheme is an example of this code. The signal level does not return to zero during a symbol transmission.

## Slide 20
Unipolar Signaling
Unipolar signaling is also called as On-Off Keying or simply OOK.
The presence of pulse represents a 1 and the absence of pulse represents a 0.
There are two variations in Unipolar signaling −
Non Return to Zero NRZ
Return to Zero RZ
Notes: Digital Communication - Line Codes | Tutorialspoint

## Slide 21: Polar - NRZ
The voltages are on both sides of the time axis.
Polar NRZ scheme can be implemented with two voltages. E.g. +V for 1 and -V for 0.
There are two versions:
  NZR - Level (NRZ-L) - positive voltage for one symbol and negative for the other
  NRZ - Inversion (NRZ-I) - the change or lack of change in polarity determines the value of a symbol. E.g. a “1” symbol inverts the polarity a “0” does not.

## Slide 22: Figure 4.6 Polar NRZ-L and NRZ-I schemes

## Slide 23: Note
In NRZ-L the level of the voltage determines the value of the bit.
In NRZ-I the inversion or the lack of inversion
determines the value of the bit.

## Slide 24: Note
NRZ-L and NRZ-I both have an average signal rate of N/2 Bd.

## Slide 25: Note
NRZ-L and NRZ-I both have a DC component problem, it is worse for NRZ-
L. Both have no self synchronization &no error detection. Both are relatively
simple to implement.

## Slide 26: Polar - RZ
The Return to Zero (RZ) scheme uses three voltage values. +, 0, -.
Each symbol has a transition in the middle. Either from high to zero or from low to zero.
This scheme has more signal transitions (two per symbol) and therefore requires a wider bandwidth.
No DC components or baseline wandering.
Self synchronization - transition indicates symbol value.
More complex as it uses three voltage level. It has no error detection capability.

## Slide 27: Figure 4.7 Polar RZ scheme

## Slide 28: Polar - Biphase: Manchester and Differential Manchester
Manchester coding consists of combining the NRZ-L and RZ schemes.
  Every symbol has a level transition in the middle: from high to low or low to high. Uses only two voltage levels. (example Ethernet LAN)
Differential Manchester coding consists of combining the NRZ-I and RZ schemes.
  Every symbol has a level transition in the middle. But the level at the beginning of the symbol is determined by the symbol value. One symbol causes a level change the other does not. (example Token Ring LAN)

## Slide 29: Figure 4.8 Polar biphase: Manchester and differential Manchester schemes

## Slide 30: Note
In Manchester and differential Manchester encoding, the transition at the middle of the bit is used for synchronization.

## Slide 31: Note
The minimum bandwidth of Manchester and differential Manchester is 2 times that of NRZ. The is no DC component.
None of these codes has error detection.