## Slide 1: DNS
.

## Slide 2
The Domain Name System (DNS) is the phonebook of the Internet. Humans access information online through domain names, like nytimes.com or espn.com. Web browsers interact through Internet Protocol (IP) addresses. DNS translates domain names to IP addresses so browsers can load Internet resources.
Each device connected to the Internet has a unique IP address which other machines use to find the device. DNS servers eliminate the need for humans to memorize IP addresses such as 192.168.1.1 (in IPv4), or more complex newer alphanumeric IP addresses such as 2400:cb00:2048:1::c629:d7a2 (in IPv6).

## Slide 3
Step 1:- Drag one Router, one Server, one Switch and four PC’s
Step 2:- Make a connection between them
Step 3:- Assign a IP to Router(Gateway Address)
Step 4:- Assign Static IP and gateway to a Server from same network
Step 5:- After that click on Services, Select DNS Give Name (lpu.in) and IP address, Click ON
Step 6:- Click on http (Services), Click Index edit option and change first content
Assign Name like(lpu.in)
Step 8:- One more address we have to add DNS server on DHCP Configuration and Save it
Step 9:- Click on a PC desktop IP , select option DHCP (apply to all the PCs)
Step 10:- Click on the PC, click on the browser, type lpu.in or IP address